## Slide 1: G-RoVe2
GRIET Robot Vehicle Version 2

## Slide 2: G-RoVe2
2 Wheel Robot Vehicle
32 bit ESP32 based control card
L298 Motor Control driver
9V battery
Ultrasonic sensor
IR sensors

## Slide 3: Projects
Remote Control using Bluetooth
Remote Control using Wi-Fi
Obstacle Avoidance
Line Following

## Slide 4: Bill of MATERIALS
Control Card with ESP32
Motor Driver
9V Battery
65mm Robot Wheels
Geared DC Motors
IR Sensors
Ultrasonic Sensor
Caster Wheels
3D printed top and bottom plates

## Slide 5: Wiring diagram

## Slide 6
 | Left Motor |  | Right Motor | 
Action | INP1 | INP2 | INP3 | INP4
Forward | HIGH | LOW | HIGH | LOW
Backward | LOW | HIGH | LOW | HIGH
Right side | HIGH | LOW | LOW | LOW
Left side | LOW | LOW | HIGH | LOW
 | Motor Pins | 
Action | INP1 | INP2
Stop | LOW | LOW
Clockwise | HIGH | LOW
Counterclockwise | LOW | HIGH
Stop | HIGH | HIGH
Single Motor action
Vehicle motion
ESP32 pin | L298 pin
GPIO14 | IN1
GPIO27 | IN2
GPIO28 | IN3
GPIO25 | IN4

## Slide 7
Bluetooth control
Bluetooth Control using mobile app
Uses Bluetooth of ESP32 on Control Card
Mobile app
G-RoVe2

## Slide 8
Bluetooth control
Offline pairing of ESP32 with mobile phone
Click on the BT Devices List button in the mobile app
From the devices list obtained select the G-Rove item
A “Connected” message will appear on the screen
Use L,F,R,W,S buttons to transfer commands
G-RoVe will receive the commands and move accordingly

## Slide 9
ESP-NOW control
ESP32 based remote with joystick
G-RoVe

## Slide 10
ESP-NOW
ESP-NOW is a wireless communication protocol defined by Espressif, which enables the direct, quick and low-power control of smart devices, without the need of a router
ESP-NOW can be used for wireless communication between two ESP family devices
ESP32 based Remote and ESP32 based G-RoVe will communicate with one another using ESP-NOW protocol
The Remote will be transmitting and G-RoVe will be receiving
Remote
G-RoVe

## Slide 11
ESP-NOW
A device participating in an ESP-NOW network can be operated in one of two modes.
Initiator – This device initiates the transmission. It will require the MAC address of the receiving device.
Responder – This device receives the transmission.
In unidirectional (half-duplex) mode, the transmitting device is the Initiator and the receiving device is the Responder.

## Slide 12
ESP-NOW
When Initiators communicate with Responders, they need to know the Responder’s MAC Address.
A MAC, or Media Access Control, Address is a unique 6-digit hexadecimal number assigned to every device on a network. It is generally burned into the device by the manufacturer
#include "WiFi.h"
void setup(){
Serial.begin(115200);
WiFi.mode(WIFI_MODE_STA);
Serial.println(WiFi.macAddress());
}
void loop(){
}

## Slide 13
ESP-NOW
// Init ESP-NOW
if (esp_now_init() != ESP_OK) {
Serial.println("Error initializing ESP-NOW");
return;
}
esp_now_register_send_cb(OnDataSent);
// Register peer
memcpy(peerInfo.peer_addr, broadcastAddress, 6);
peerInfo.channel = 0;
peerInfo.encrypt = false;
// Add peer
if (esp_now_add_peer(&peerInfo) != ESP_OK){
Serial.println("Failed to add peer");
return;
}

## Slide 14
ESP-NOW

## Slide 15
Object detection using Ultrasonic sensor (HC-SR04)
The sensor has 4 pins. VCC and GND go to 5V and GND pins on the Arduino.
Trig and Echo go to any digital Arduino pin.
Using the Trig pin we send the ultrasound wave from the transmitter, and with the Echo pin we listen for the reflected signal.
A short ultrasonic sound wave being transmitted towards the target. The target reflects back the wave which confirms the presence of the object.
OBSTACLE detection – Ultrasonic sensor
ESP32 pin | Ultrasonic
VIN | VCC
GPIO12 | Trig
GPIO13 | Echo
GND | GND

## Slide 16
OBSTACLE detection – Ultrasonic sensor
To use this sensor to measure distance, the robot's brain must measure the amount of time it takes for the ultrasonic sound to travel.
Sound travels at approximately 340 meters per second (0.034 mm per microsecond).
To measure the distance the sound has travelled we use the formula:
Distance = (Time x Speed Of Sound) / 2.
= (time * 0.034) / 2
The "2" is in the formula because the sound has to travel back and forth.

## Slide 17
Line following – IR sensor
Line following using IR sensors.
The white LED is an IR LED which continuously emits the IR light and black LED is a photodiode that works as the receiver in the IR sensor.
If the light gets reflected back by hitting any object in front it, the IR receiver receives this light. This way the object is detected in the case of the IR sensor.
Using potentiometer (Trimpot) we can control the range
i.e. from how far you want to detect the object by
changing the value of the potentiometer.

## Slide 18
Line Follower
The concept of working of line follower is related to light. We use here the behavior of light at the black and white surfaces. When light falls on a white surface it is almost fully reflected and in the case of a black surface light is completely absorbed. This behavior of light is used in building a line follower robot.
IR Sensor Status
When IR Sensor on white surface, then its status is LOW.
When IR Sensor on Black surface, then its status is HIGH.

## Slide 19
we are using two IR sensor modules namely the left sensor and the right sensor.
When both left and right sensor senses white then the robot moves forward.
2. If the left sensor comes on a black line then the robot turn the left side.
3. If the right sensor sense black line then robot turn right side until both sensors comes at the white surface. When the white surface comes robot starts moving on forward again.
4. If both sensors come on the black line, the robot stops.
1
2
3
4
Line following – IR sensor

## Slide 20
Line following – IR sensor
Action | IR Sensor 1 (Right) | IR Sensor 2 (Left)
Forward | LOW | LOW
Left side | HIGH | LOW
Right side | LOW | HIGH
Stop | HIGH | HIGH
Vehicle motion